## Slide 1
Debugging P4 programs with Vera
Radu Stoenescu, Dragos Dumitrescu, Matei Popovici, Lorina Negreanu, Costin Raiciu
University Politehnica Bucharest
Vera overview
0
2
PROGRAMMING MODEL FOR P4 DEVICES
P4 device overview
0
2
BUGS CAUGHT USING VERA
SOFTWARE DEFINED NETWORKS:
OPEN FOR PROGRAMMABILITY, OPEN FOR BUGS
Legacy network devices
0
2
P4 device
0
2
Control plane
Data plane
Controller
Programmable data pane
P4 program
P4 to SEFL Compiler
P4 table entries
Symnet verification engine
Network
Policy
All possible paths for all possible packets
P4 Controller
STATIC ANALYSIS OF P4 PROGRAMS USING VERA
Vera
P4 quirks
0
2
Parse-able input space decoupled from
processing pipeline.
Invalid packet header access.
Invalid encapsulation.
A P4 program defines a superset of the
actual runtime behavior.
Packet loops, black holes.
Erroneous table states.
BGP, OSPF, EIGRP, …
ASIC implementation
Centralized,
X86 programmable
Programmable
P4 switch API
Vera in depth
0
2
Reasoning about switch behavior without
runtime information.
Proactively populate tables with symbolic
entries.
Scaling symbolic execution for tables with
hundreds of thousands of entries.
Use domain specific data structure for
computing path conditions.

## Slide 2
WHAT CAN GO WRONG?
P4 packet processing pipeline
0
2
Programmable
parser
Packet (byte[])
Headers
eth
ipv4
Programmable
match-action
units
Packet
reassembly
Packet
Payload
Metadata
eth
tag
ipv4
err
bcast
port