## Slide 1: VOR Base Stations for Indoor 802.11 Positioning
Dragoş Niculescu - NEC Labs
Badri Nath - Rutgers University
*this research work was supported by a grant from NSF.

## Slide 2: existing indoor positioning
Extra infrastructure - Cricket(MIT), Active badge(Cambridge)
  good accuracy
  instrumentation
  specialized beacons, badges
  LOS (line of sight)
Signal strength (SS) map - Radar(Microsoft), Rice
  existing 802.11 base stations
  map depends on people, furniture
  centralized database
requires either:
Notes: RADAR - Microsoft
CRICKET - MIT

## Slide 3: signal strength map example(RADAR)
build SS map: for each point, store SS to all 5 BS
query: measure SS to all BS best match in the map
Notes: RADAR

## Slide 4: VORBA = VOR base stations
Goals:
no signal strength map
limited infrastructure
instead, use sophisticated 802.11 base station
positioning using
  angles
  ranges
  angles and ranges
Notes: We have a prototype

## Slide 5: VORBA prototype
laptop + directional antenna
record player
antenna pattern

## Slide 6: basic idea (angle based)

## Slide 7: practical scenario
SS()=signal strength variation
peak  angle
mean  range
angle
3. and / or   position
range
1. SS()
2.
Notes: SS(alfa) is a periodic function

## Slide 8: best peak distribution
4.5 peaks on average
best peak is first/second 90% of the time

## Slide 9: other peak distribution
most other peaks point away from the true direction

## Slide 10: experiments
32 measurement points
5 main base stations
N/E/S/W measurements of 3-4 revolutions each

## Slide 11: angles only positioning
3.5m median position error
3m if we knew the best peak

## Slide 12: quantized angles
simulation:
  measurements rounded to 90°, 45° and 22.5°
  little degradation for 22.5° and 45°

## Slide 13: can it do better?
VORBA provides positions using:
  discrete angles  3.5m
  quantized angles
  angle distribution (see paper)
can it provide ranges?

## Slide 14: range inference
open space attenuation
d(SS)
  obtained by fitting
  known to be unreliable
we obtain it from integration of SS()
offline: 5-fold cross validation
  SS from one BS used to derive ranges for all others
  2.8m median range error
  4.5m median position error

## Slide 15: angles and ranges
angle error sa = 0.4 radians = 21°
range error sr = 0.2r
approximate uncertainty as an ellipse
error ellipse increases with distance

## Slide 16: angles and ranges uncertainty
How to combine several readings? simplified Kalman filter.

## Slide 17: 3.5m+4.5m=2.1m? (angles and ranges)
more base stations  better positions
2.1m median position error (all 7BS)

## Slide 18: discussion
triangulation with large outliers
use more than two angles?
no correlation between
  angle error and distance
  angle error and SS
corridors  waveguides
revolving signal at the mobile?
data performance?

## Slide 19: summary
VORBA = VOR base station
move complexity into the base station
  less infrastructure
  no signal strength map
prototype = revolving base station
  measure SS() to derive
    discrete angles
    angle distribution
    ranges
  median position error 2.1m - 3.5m
works with quantized angles

## Slide 20: index
existing positioning solutions
  SS map example
VORBA goals
prototype
basic idea
  practical scenario
peak distribution
experiments
  angle only
  quantized angles
  ranges
  angles and ranges
discussion
summary